## Slide 1: TrackSeed
AR cone placement and a track digital twin for Formula Student
State of the art and project proposal
André Lopes · Tomás Santos
Emerging and Intelligent Technologies · Virtual and Augmented Reality · 2026/2027
Notes: About 15 seconds. Introduce ourselves and the project: TrackSeed lets one person set out a Formula Student track with augmented reality on a phone, while a digital twin of the track follows the placement live in the cloud. This talk covers the problem, what the literature says, the design decisions that follow, and how we will validate them.

## Slide 2: A track is only a pattern of cones
FS Driverless 2026 specification
Small blue: left border
Small yellow: right border
Small orange: entry and exit lanes
Big orange: start, finish and timekeeping lines
At most 5 m between cones; less in corners
Tape and trigonometry
The plan is transferred to the ground by hand
Several people, lost test time
Each layout is rebuilt many times per season
No check of the result
A wrong cone is fixed only if someone notices
Driverless cars use the cones as landmarks. A layout that differs from the plan changes the problem the car is solving.
Sources: FS Driverless Specification 2026; Kabzan et al., 2020
Notes: About 1 minute. A Formula Student track exists only as coloured cones: blue on the left, yellow on the right, orange for lanes, big orange at start and finish, at most 5 m apart. In our team we set these out by hand with tapes and trigonometry. It needs several people, takes time from testing, and there is no check: a wrong cone is only fixed if someone notices. For a driverless car that matters, because perception and path planning are built on those cones, so a wrong layout changes the problem and makes test days hard to compare.

## Slide 3: TrackSeed: one person, one phone
1. Upload plan
Track as JSON on the web dashboard
2. Align
Scan two markers at the start line
3. Place and verify
AR shows each cone; the phone checks it
4. Live twin
Dashboard follows; edits flow back
5. Identify car, report
Classifier links the session to the car
VAR
AR guidance aligned to the ground, and the digital twin of the track
EIT
Cloud platform, real-time sync, remote configuration and on-device vision
Notes: About 1 minute. Before the test day, the team lead uploads the plan. On the field, one person aligns it by scanning two markers, then walks the track while the phone shows each cone in AR. When a cone is put down, an on-device model checks it and the result goes to the cloud. The team lead follows a live twin on the dashboard and can edit it, which updates the guidance. Finally the phone identifies which team car is running and produces a report. VAR provides the AR and the twin; EIT provides the cloud, synchronisation and on-device vision.

## Slide 4: How we reviewed the literature
25
sources selected
19
peer-reviewed papers, chapters and reviews
1
preprint
5
specifications and official docs
Themes
AR for on-site layout
Mobile AR tracking
Digital twins
Real-time sync
Edge AI
Fine-grained car classification
Google Scholar and publishers' libraries, October 2026. Kept if relevant, comparable, credible and recent (2015 onwards preferred). Almost no studies cover motorsport track setout, so most evidence comes from construction layout.
Notes: About 45 seconds. We searched Google Scholar and publisher libraries in October 2026, with search strings built from the main concepts, and followed references. We kept 25 sources: 19 peer-reviewed, one preprint and five specifications or official documents, which we used only for capabilities and rules, not as evidence of performance. One limitation up front: almost nobody has studied track setout, so most evidence comes from construction layout, which is the closest task.

## Slide 5: Phones place AR content within ~16 cm
Chart: Outdoor utility placement, 32 students
| HoloLens 2 | Trimble SiteVision (GNSS) | iPad Pro | iPhone 13 Pro Max
Other devices | 8.3 | 8.9 | 9.1 | 0
Phone | 0 | 0 | 0 | 15.9
Our tolerance: 10–15 cm
The phone result is right at the limit, and it was measured over a small area
Indoors, near a marker: ≈5 cm
HoloLens with a paper marker; error grew farther from the marker
Takeaway
AR guidance is feasible, but not accurate enough by default at track scale
Sources: Kim and Olsen, ISARC 2025; Chalhoub and Ayer, ITcon 2019
Notes: About 1 minute 15. The closest evidence is construction layout. Kim and Olsen had 32 students place objects outdoors where they saw virtual pipes, and measured them with a total station. The HoloLens 2 was best at 8.3 cm; the iPhone was worst at about 16 cm. Indoors, Chalhoub and Ayer got about 5 cm with a HoloLens and a paper marker, worse farther from the marker. Our provisional tolerance is 10 to 15 cm, so the phone is right at the limit, over an area much smaller than a track. AR guidance is feasible, but not accurate enough by default.

## Slide 6: Tracking error grows with distance
≈17 m
per 120 m walked
ARCore, ARKit and HoloLens in a 1,600 m² hall
Feigl et al., 2020
4.8 vs 25.1 cm
drift after walking away and back
ARCore vs ARKit, 200+ indoor scenes; worse with low texture
Scargill et al., 2021 (preprint)
1.1–2.1 cm
static RMS error
Smartphone RTK GNSS in open sky; no drift, needs corrections
Jiang et al., 2023
One alignment at the start line cannot hold a 200 m+ track. The plan must be re-aligned along the track, or anchored to absolute positions. Uniform asphalt is a further drift risk.
Notes: About 1 minute. The studies seem to disagree, metres versus centimetres, but the difference is scale. Feigl et al. walked up to 60 m in a big hall and found about 17 m of error per 120 m. Scargill et al. measured only room scale: a few centimetres, and ARCore drifted less than ARKit when the user walked away and came back. They also found more drift in low-texture scenes, which is a risk on asphalt. RTK GNSS on a phone reaches 1 to 2 cm with no drift, but needs a correction service. Conclusion: we must re-align along the track.

## Slide 7: A twin needs data flowing both ways
Digital model
Physical
Virtual
No automatic data exchange
solid = automatic, dashed = manual
Digital shadow
Physical
Virtual
Updated automatically from the physical object
solid = automatic, dashed = manual
Digital twin
Physical
Virtual
Automatic exchange in both directions
solid = automatic, dashed = manual
TrackSeed: confirmed cones go to the dashboard, and dashboard edits (move, add, remove) change the guidance on the phone. Without the second direction it would only be a shadow.
Sources: Kritzinger et al., 2018; Grieves and Vickers, 2017; Tao et al., 2019
Notes: About 1 minute. The term digital twin is often used loosely. Kritzinger et al. separate three cases: a model with no automatic data exchange, a shadow that is updated automatically from the physical object, and a twin, where data flows automatically in both directions. They found most published systems are only models or shadows. For TrackSeed this sets a concrete requirement: a dashboard that only shows confirmed cones is a shadow. To be a twin, edits on the dashboard must reach the phone and change the guidance on the field.

## Slide 8: Sync over WebSocket, inference on the phone
Phone ↔ cloud ↔ dashboard
 | WebSocket | MQTT
Latency | Lower | Slightly higher
Throughput, resources | Lower | Higher, fewer resources
Browser client | Native | Needs a broker
Decision: WebSocket for live updates, REST for files, offline queue on the phone. One small message per cone.
Edge vs cloud inference
Cloud: More compute, but adds latency, uplink cost and privacy risk
On the phone: No network needed; mobile NPUs approach desktop GPUs
Test fields: Mobile coverage is often weak
Decision: both vision models run on the phone with LiteRT; the cloud retrains and pushes new versions. FSOCO cone data as a starting point.
Sources: Ajayi et al., 2023; Chen and Ran, 2019; Ignatov et al., 2019; Vödisch et al., 2022
Notes: About 1 minute. For synchronisation, the only controlled comparison found MQTT had higher throughput and used fewer resources, while WebSocket had lower latency. We send one small message per cone to a browser, so WebSocket fits better; the phone keeps a local queue and replays it when the connection returns. For inference, sending frames to the cloud adds latency and privacy risk, while phones now have capable accelerators. Since test fields often have weak coverage, both models run on the phone and the cloud only retrains them.

## Slide 9: Main vision task: which car is running?
Why it is hard
Fine-grained: the classes differ only in details
Cars from the same team often look alike
Accuracy depends on viewpoint (CompCars)
No public dataset has our cars, so we build our own
Collect
Photos and video frames of each car, all viewpoints, several test days, plus an unknown class
Fine-tune
ImageNet-pretrained MobileNetV2-class network (72% top-1, 3.4M parameters)
Run on the phone
Exported to LiteRT; target ≤100 ms per image
Confirm and grow
Low confidence: the user confirms; new images join the dataset
Split by test day, not at random: frames from one session in both sets would overestimate accuracy.
Sources: Yang et al., CVPR 2015; Yosinski et al., NeurIPS 2014; Sandler et al., CVPR 2018
Notes: About 1 minute 15. Besides the cone check, our main computer vision task is classifying which team car is being used, so each session is linked to its vehicle. It is a fine-grained problem: on CompCars, accuracy depended strongly on the viewpoint. No public dataset has our cars, so we build our own: photos and video frames of each car from all angles, on several days, plus an unknown class. With little data, transfer learning is the standard answer: we fine-tune a pretrained MobileNetV2-class network and run it on the phone. We split by test day, so the score reflects a new day, not memorised backgrounds.

## Slide 10: From evidence to design decisions
Gap: no study tested phone AR setout over a full track, or combined guidance, verification, vehicle ID and a two-way twin.
Evidence | Decision
AR accuracy degrades with distance from the marker | Two-point alignment at the start
Tracking error grows with distance walked | Re-alignment markers; RTK as an option
WebSocket has lower latency; the client is a browser | WebSocket, with an offline queue on the phone
Only two-way data flow makes a twin | Dashboard edits update the guidance
On-device inference avoids network cost; weak coverage | Cone check on the phone; models updated remotely
Pretrained features transfer; viewpoint drives accuracy | Self-made all-view dataset; fine-tuned mobile CNN
Notes: About 1 minute. The gap: no study has tested phone-based setout over a full track, and none combines guidance, verification of each object, vehicle identification and a live two-way twin. Each finding leads to a decision: distance-dependent error leads to two-point alignment and re-alignment markers; the protocol comparison leads to WebSocket with an offline queue; the twin definition requires edits to flow back; edge inference keeps the models on the phone; and transfer learning plus viewpoint effects shape the car dataset.

## Slide 11: Two markers, re-aligned along the track
1°
heading error at a single start marker puts a cone 200 m away
≈3.5 m
off its planned position, before any drift is added
Two-point alignment + re-alignment markers
Fixes position and heading; drift limited to marker spacing
Adopted
Smartphone RTK GNSS
Centimetre accuracy, no drift; needs a receiver and corrections
Optional
Single start marker
Heading error and drift grow along the track
Rejected
ARCore Geospatial API
No published cm-level accuracy; needs Street View
Rejected
Notes: About 1 minute. Why not a single marker at the start line? It fixes the heading of the whole plan from something less than a metre wide. A heading error of just one degree moves a cone 200 m away by about 3.5 m, before drift. Two markers placed far apart fix position and heading together, and further markers along the track limit drift to the distance between them. RTK stays an optional extension, and the Geospatial API is rejected because there is no evidence it reaches centimetre accuracy. Marker spacing will be set from field tests.

## Slide 12: Conceptual architecture
Android app
AR alignment and guidance, cone check, car recognition, offline store
Cloud platform
REST API, WebSocket sync, twin database, car dataset, model store
Web dashboard
2D live twin, track editor, session reports
Notes: About 1 minute. Three components. The Android app does AR alignment and guidance, the cone check, car recognition and the offline store; tracking and inference stay on the phone. The cloud, in Docker containers, holds the REST API, the WebSocket sync service, the twin state, the car dataset and the model store. The dashboard shows and edits the twin. Confirmed cones flow right, edits and model updates flow back left. Tags show which course unit owns each part. Out of scope: several phones at once, iOS, and the Geospatial API.

## Slide 13: How we will validate it
H1
Placement accuracy
≤15 cm median
no cone over 30 cm
Skidpad and autocross section vs surveyed reference points
H2
Setup time
≥30% faster
than the tape method
One person with TrackSeed vs the team's usual method, same track
H3
Twin latency
≤1 s median
cone to dashboard
Timestamps on Wi-Fi and mobile data
H4
Car identification
≥95% accuracy
≤100 ms on the phone
Self-made dataset, held-out test days only
All success indicators are provisional and will be reviewed after the first field test
Notes: About 1 minute. Four hypotheses. H1, the question the literature leaves open: phone setout with re-alignment keeps cones within tolerance over a full track; median at most 15 cm, none over 30. H2: one person with TrackSeed is at least 30% faster than our tape method. H3: a confirmed cone appears on the dashboard within about one second. H4: the car classifier reaches at least 95% accuracy on test days it never saw, in under 100 ms on the phone. Unlike the reviewed studies, these tests run on a full track in its real environment.

## Slide 14: Risks and plan
Main risks
Drift on low-texture asphalt; not measured in any study
Outdoor light, screen glare and winter rain
Cone data come from car-mounted cameras
Small car dataset; similar-looking cars
User looks at the screen while walking: closed track only
Plan
Oct
Track format, AR alignment on a skidpad, start collecting car images
Nov
Cone verification, car classifier, cloud platform and sync
Dec
Dashboard twin, full autocross tests
Jan
Validation and report
Notes: About 1 minute. The main technical risk is accuracy over distance, and nobody has measured phone AR on asphalt, which has little texture. Outdoor light, glare and rain can affect both tracking and the vision models; the cone data come from car-mounted cameras, not a handheld phone; and the car dataset is small, with similar cars, which is why we split by test day. Safety: the user looks at the screen while walking, so it is for closed tracks only. The plan runs from AR alignment in October to validation in January, collecting car images on every test day.

## Slide 15: Takeaways
Phone AR is feasible but unproven at track scale
Error grows with distance, so we align on two markers and re-align along the track
A true two-way digital twin
Confirmed cones reach the dashboard; dashboard edits reach the phone over WebSocket
Two on-device vision tasks
Cone verification and car identification from a self-made dataset
Next: AR alignment on a skidpad, measure drift on our test site, collect car images every test day.
Questions?
Notes: About 45 seconds. To sum up: the literature shows phone AR placement is feasible but unproven at track scale, so we align on two markers and re-align. The system is a true twin, with edits flowing back to the phone. And there are two on-device vision tasks, with car identification as the main one, trained on our own dataset. Next we implement alignment on a skidpad, measure drift on our site, and keep collecting car images. Thank you, we're happy to take questions.